Orthopaedic Sports Specialists, P.C.

Michael E. Joyce, M.D. & Alex G. Dukas, M.D.

84 Glastonbury Blvd., Suite 101,  Glastonbury, Connecticut  06033

Voice:  860-652-8883,   Fax:  860-652-8887

Clavicle Open Reduction Internal Fixation

Post Operative Rehabilitation Protocol:

Range of motion:

- Begin pendulums and gentle passive and active-assisted range of motion immediately, emphasizing forward elevation.

- Do not initiate strengthening or active range of motion until six weeks post-operatively and cleared by Dr. Dukas.

Strengthening:

- Begin strengthening at six weeks post-operatively, starting with isometrics and progressing to bands and then weights, with a focus on the scapular stabilizers, rotator cuff, and deltoid.

- Please provide and emphasize a home exercise program. This program should focus on: o Regaining forward elevation (pulleys, wall climbs, table slides, etc.)

- Regaining external rotation using passive and active external rotation exercises (canes, door frame stretches, etc.)

- Ok to return to light athletic activities at three months if full range of motion has been recovered, heavier athletic activities at four months.